## Slide 1: CSC258 Project
By Brendan Neal and Filip Tomin

## Slide 2: Project Description – Logic Gate Quiz
Win Condition
  Solve all 9 gates in 2 minutes
Rules
  Logic gates are given randomly
  Player uses board switches to test the IO of the gate
  Player inputs a number corresponding to the gate
  Right number -> move on to next gate
  Wrong number -> player must select another gate number (with no IO support!)

## Slide 3: Block Diagram - Timer
6-Counter
10 Counter
10 Counter
10 Counter
2-Counter
Ten Sec
C-Sec Rate Divider
Out Pulse
50Mhz Clock
Reset / Enable
Reset Val = 2
Reset Val = 0
Sec
D-Sec
Minutes
C-Sec

## Slide 4: Block Diagram – Gate Selector
2 9-Muxes (1-hot)
NAND
NOR
NXOR
AND
OR
XOR
SR
T
D
In[1:0]
Gate Output
8 Bits

## Slide 5: Block Diagram – Gate Control
Gate Selector
Inputs[1:0]
Confirm
Select Gate
Manipulates 1-hot Vector
“Locks in” Gate selection
Gate Output
VGA Blank Out
VGA Control FSM (NYI)
Timer
Timer Enable
VGA Output
Current Gate (RNG)

## Slide 6: Block Diagram – VGA FSM (NYI)
Draw Wire 1
Draw Wire 2
Draw Wire 3
Rectangle Dimension/Color Determination Modules
Rectangle Drawer Module
VGA Output
X
Y
Location
Length
Width
Color
Draw Completion Rectangle
Constants
I/O Wire Values
Done Signal (acts like clock)
On Selection Edge

## Slide 7: Interesting Aspects
Two minute timer (not hex!)
  Designed with modularity in mind – can be changed to any time limit!
  Harder to get working than we thought
Gate Selector
  Works flawlessly
  Easy to incorporate in the final design

## Slide 8: Difficulties (first milestone)
Board switches were inconsistent
  Made testing the gate select difficult
Timer odd-second skip issue
  Timer would skip every odd second (e.g. 38 sec -> 36 sec -> …)
Not being able to properly simulate the timer in MS
  Timer values were completely uncertain in MS but the timer actually worked on the board
  Meant we could only do our testing and editing during lab hours
MS compiles differently compared to QP
  We had to edit code that compiled in MS in order for it to compile in QP

## Slide 9: Difficulties (second milestone)
Timer odd-second skip issue was still occurring
  Managed to fix it by changing <= to = for assignments in an always block (???)
Getting our background loaded on to the VGA
  Had some misunderstandings about the maximum resolution allowed
Figuring out how to properly draw things on the VGA
  Stuff can’t be drawn in parallel!

## Slide 10: Difficulties (last milestone)
Timer broke again
  We loaded the newer code onto the board and it still had the same odd-skip issue
  Random lines started appearing on HEX5 (even though we never used it in our code)
Getting the gate control working
  We decided to abandon the VGA implementation because it would take too much time, and use the board IO instead
  MS once again failed to produce any meaningful results when testing (uncertain values)
  When restricted to using the boards we were unable to debug this component in time
Boards wouldn’t load our project (third lab session)
  We have no idea why this happened – our code was compiling but not loading
Note: we have a more recent version of our DemoGateControl.v on the lab computers but it doesn’t work as it can’t load onto the board

## Slide 11: ModelSim Uncertainty Images
MS gate control simulation uncertainties
MS timer simulation uncertainties
Underlying component of timer works properly

## Slide 12: Lessons Learned
MS compiles differently than QP
Things that work on MS may not work on QP and vice versa
<= may not always be appropriate for an always block
Sometimes the board is the source of your problems
Sometimes uncertain things in MS work on the board

## Slide 13: Component Authorship
Milestone / Lab | Filip Tomin | Brendan Neal
First | Gate Selection | Timer
Second | Fixing timer | VGA (code and mif image)
Third | Random Generation and VGA, AbstractGateControl | VGA, DemoGateControl