## Slide 1: CSC258 Project
By Brendan Neal and Filip Tomin

## Slide 2: Project Description – Logic Gate Quiz
Win Condition
  Solve all 9 gates in 2 minutes
Rules
  Logic gates are given randomly
  Player uses board switches to test the IO of the gate
  Player inputs a number corresponding to the gate
  Right number -> move on to next gate
  Wrong number -> player must select another gate number (with no IO support!)

## Slide 3: Block Diagram - Timer
6-Counter
10 Counter
10 Counter
10 Counter
2-Counter
Ten Sec
C-Sec Rate Divider
Out Pulse
50Mhz Clock
Reset / Enable
Reset Val = 2
Reset Val = 0
Sec
D-Sec
Minutes
C-Sec

## Slide 4: Block Diagram – Gate Selector
2 9-Muxes (1-hot)
NAND
NOR
NXOR
AND
OR
XOR
SR
T
D
In[1:0]
Gate Output
8 Bits

## Slide 5: Block Diagram – Gate Control
Gate Selector
Inputs[1:0]
Confirm
Select Gate
Manipulates 1-hot Vector
“Locks in” Gate selection
Gate Output
VGA Blank Out
VGA Control FSM (NYI)
Timer
Timer Enable
VGA Output
Current Gate (RNG)

## Slide 6: Block Diagram – VGA FSM (NYI)
Draw Wire 1
Draw Wire 2
Draw Wire 3
Rectangle Dimension/Color Determination Modules
Rectangle Drawer Module
VGA Output
X
Y
Location
Length
Width
Color
Draw Completion Rectangle
Constants
I/O Wire Values
Done Signal (acts like clock)
On Selection Edge

## Slide 7: Interesting Aspects
Two minute timer (not hex!)
  Looks cool
  Harder to get working than we thought
Gate Selector
  Works flawlessly
  Easy to incorporate in the final design

## Slide 8: Difficulties
Board switches were inconsistent
Timer odd-second skip issue (<= vs. = assignment)
Getting our background on the VGA
Having to edit code to work on QP even though it worked on MS
Not being able to simulate certain things on MS
Uncertain MS simulations that work fine on the board

## Slide 9: Lessons Learned
MS compiles differently than QP
Things that work on MS may not work on QP and vice versa
<= may not always be appropriate for an always block
Sometimes the board is the source of your problems
Sometimes uncertain things in ModelSim work on the board